ASTERICS
Module Description

Module name: as_threshold

Author:	Michael Schaeferling
Date:	2017-01-17

Module description:
This module thresholds image data by taking two threshold values into account. The lower threshold t1 and the upper threshold t2 separate the occuring image data values into 3 ranges:
a) below lower threshold t1 [image_data < t1]
b) between lower threshold t1 and upper threshold t2 [t1 >= image_data <= t2]
c) above upper threshold t2 [image_data > t2]

For each range a, b and c, it can be specified whether original image data or a fixed, user determined value is to be output.

Example:
This graph depicts a configuration where image

Output
intensity
data below t1, corresponding range „a“, is set to a
fixed output value.

For values between t1 and t2, corresponding range
„b“, output values are set to be the original input
image data.

Values above t2, corresponding range „c“, are also
set to a fixed value in the output data.
a
(<t1)
C
(>t2)
b
(>=t1
&&
<=t2)

Input
intensity
t1
t2

Module design specification:
- In and out data bit width is limited to a maximum of 12 bits.
- This module is implemented using combinatorial logic only. There are no registers delaying data or control signals.
- Parameters:
  - Thresholds t1 and t2
  - Flags for ranges a, b and c to output fixed values or original image data
  - Values for ranges a, b and c for fixed data output

- Configuration register outline:
  - Register_1:
    - [11:0]	t1
    - [23:12]	t2
    - [27:24]	c_upper(11:8)
    - [28]	fixval_a_enable
    - [29]	fixval_b_enable
    - [30]	fixval_c_enable
  - Register_2:
    - [11:0]	a
    - [23:12]	b
    - [27:24]	c_lower(7:0)