Pmod-Adapter-Board
for OV7670 camera module

Version: 0.3
Changes to previous version:
- Pinout redesign to allow (one layer) PCB design.
- All signal lines contain resistors to protect against short circuits

Pmod Connectors used for OV7670 sensor connection:
Pin	6	5	4	3	2	1		Pin	6	5	4	3	2	1
Zybo (JC)			T10	T11	W15	V15		Zybo (JB)			W20	V20	U20	T20
uZed (JB)			Y14	W14	Y17	Y16		uZed (JA)			U12	T12	T10	T11
	3V3	GND	D0	D2	D4	D6			3V3	GND	VSYNC	HREF	PCLK	XCLK
	3V3	GND	D1	D3	D5	D7			3V3	GND	SIOD	SIOC	RESET	PWDN
Pin	12	11	10	9	8	7		Pin	12	11	10	9	8	7
Zybo (JC)			U12	T12	Y14	W14		Zybo (JB)			W19	W18	Y19	Y18
uZed (JB)			W15	V15	U17	T16		uZed (JA)			T15	T14	W13	V12

Caution: For I2C communication with the sensor, make sure to properly pull-up SIOD and SIOC with 4.7kOhm resistors (here R1 and R2).

BOM:
2x (R1, R2):	SMD resistor, 0805, 4,7 kOhm, 125 mW
14x (R3-R16):	SMD resistor, 0805, 100 Ohm, 125 mW
2x (R17, R18):	SMD resistor, 0805, 100 Ohm, 125 mW
1x	Female pin header, 2x9 pin, 2,54mm
2x	Male pin header, 2x6 pin, 2,54mm